To include the desired backup schedule with appropriate pools in your Bacula configuration, we'll need to set up the necessary job definitions, schedules, and pools. Here are the updated steps:
### 1. Install Bacula on the Backup Server
#### 1.1. Update and Install Bacula
bash
sudo apt update
sudo apt install bacula-server bacula-client
#### 1.2. Configure Bacula Director (/etc/bacula/bacula-dir.conf)
Edit the Bacula Director configuration file to define the jobs, file sets, schedules, and pools:
bash
sudo nano /etc/bacula/bacula-dir.conf
Add the following configurations:
bash
# Define the file sets for each server and workstation
FileSet {
  Name = "DataServerSet"
  Include {
    Options {
      signature = MD5
    }
    File = /data
  }
}

FileSet {
  Name = "NFSServerSet"
  Include {
    Options {
      signature = MD5
    }
    File = /media
  }
}

FileSet {
  Name = "ClientSet"
  Include {
    Options {
      signature = MD5
    }
    File = /home
    File = /etc
  }
}

# Define the pools
Pool {
  Name = "DailyPool"
  PoolType = Backup
  Recycle = yes
  AutoPrune = yes
  Volume Retention = 7 days
  Maximum Volume Bytes = 50G
  Maximum Volumes = 5
}

Pool {
  Name = "WeeklyPool"
  PoolType = Backup
  Recycle = yes
  AutoPrune = yes
  Volume Retention = 30 days
  Maximum Volume Bytes = 100G
  Maximum Volumes = 4
}

Pool {
  Name = "MonthlyPool"
  PoolType = Backup
  Recycle = yes
  AutoPrune = yes
  Volume Retention = 180 days
  Maximum Volume Bytes = 200G
  Maximum Volumes = 6
}

# Define the schedules
Schedule {
  Name = "DailySchedule"
  Run = Incremental daily at 23:00
}

Schedule {
  Name = "WeeklySchedule"
  Run = Differential 1st sun at 23:05
}

Schedule {
  Name = "MonthlySchedule"
  Run = Full 1st sun at 23:10
}

# Define the jobs for each server and workstation
Job {
  Name = "BackupDataServer"
  JobDefs = "DefaultJob"
  FileSet = "DataServerSet"
  Client = DataServer-fd
  Schedule = "DailySchedule"
  Storage = File
  Messages = Standard
  Pool = DailyPool
}

Job {
  Name = "BackupDataServerWeekly"
  JobDefs = "DefaultJob"
  FileSet = "DataServerSet"
  Client = DataServer-fd
  Schedule = "WeeklySchedule"
  Storage = File
  Messages = Standard
  Pool = WeeklyPool
}

Job {
  Name = "BackupDataServerMonthly"
  JobDefs = "DefaultJob"
  FileSet = "DataServerSet"
  Client = DataServer-fd
  Schedule = "MonthlySchedule"
  Storage = File
  Messages = Standard
  Pool = MonthlyPool
}

Job {
  Name = "BackupNFSServer"
  JobDefs = "DefaultJob"
  FileSet = "NFSServerSet"
  Client = NFSServer-fd
  Schedule = "DailySchedule"
  Storage = File
  Messages = Standard
  Pool = DailyPool
}

Job {
  Name = "BackupNFSServerWeekly"
  JobDefs = "DefaultJob"
  FileSet = "NFSServerSet"
  Client = NFSServer-fd
  Schedule = "WeeklySchedule"
  Storage = File
  Messages = Standard
  Pool = WeeklyPool
}

Job {
  Name = "BackupNFSServerMonthly"
  JobDefs = "DefaultJob"
  FileSet = "NFSServerSet"
  Client = NFSServer-fd
  Schedule = "MonthlySchedule"
  Storage = File
  Messages = Standard
  Pool = MonthlyPool
}

Job {
  Name = "BackupClient"
  JobDefs = "DefaultJob"
  FileSet = "ClientSet"
  Client = Client-fd
  Schedule = "DailySchedule"
  Storage = File
  Messages = Standard
  Pool = DailyPool
}

Job {
  Name = "BackupClientWeekly"
  JobDefs = "DefaultJob"
  FileSet = "ClientSet"
  Client = Client-fd
  Schedule = "WeeklySchedule"
  Storage = File
  Messages = Standard
  Pool = WeeklyPool
}

Job {
  Name = "BackupClientMonthly"
  JobDefs = "DefaultJob"
  FileSet = "ClientSet"
  Client = Client-fd
  Schedule = "MonthlySchedule"
  Storage = File
  Messages = Standard
  Pool = MonthlyPool
}

# Define the clients
Client {
  Name = DataServer-fd
  Address = dataserver.example.com
  FDPort = 9102
  Catalog = MyCatalog
  Password = "DataServerPassword"
  File Retention = 60 days
  Job Retention = 6 months
  AutoPrune = yes
}

Client {
  Name = NFSServer-fd
  Address = nfsserver.example.com
  FDPort = 9102
  Catalog = MyCatalog
  Password = "NFSServerPassword"
  File Retention = 60 days
  Job Retention = 6 months
  AutoPrune = yes
}

Client {
  Name = Client-fd
  Address = client.example.com
  FDPort = 9102
  Catalog = MyCatalog
  Password = "ClientPassword"
  File Retention = 60 days
  Job Retention = 6 months
  AutoPrune = yes
}
#### 1.3. Configure Bacula Storage Daemon (/etc/bacula/bacula-sd.conf)
Edit the Bacula Storage Daemon configuration file to define the storage device:
bash
sudo nano /etc/bacula/bacula-sd.conf
Add the following configuration:
bash
Device {
  Name = FileStorage
  MediaType = File
  ArchiveDevice = /mnt/backup
  LabelMedia = yes
  RandomAccess = yes
  AutomaticMount = yes
  RemovableMedia = no
  AlwaysOpen = no
}
#### 1.4. Configure Bacula File Daemon (/etc/bacula/bacula-fd.conf)
The File Daemon configuration on the backup server should remain as default.
#### 1.5. Start Bacula Services
bash
sudo systemctl start bacula-dir
sudo systemctl start bacula-sd
sudo systemctl start bacula-fd

sudo systemctl enable bacula-dir
sudo systemctl enable bacula-sd
sudo systemctl enable bacula-fd
### 2. Install and Configure Bacula File Daemon on Data Server
#### 2.1. Install Bacula Client
bash
sudo apt update
sudo apt install bacula-client
#### 2.2. Configure Bacula File Daemon (/etc/bacula/bacula-fd.conf)
Edit the Bacula File Daemon configuration file:
bash
sudo nano /etc/bacula/bacula-fd.conf
Add the following configuration:
bash
FileDaemon {
  Name = DataServer-fd
  FDport = 9102
  WorkingDirectory = /var/lib/bacula
  PidDirectory = /var/run/bacula
  MaximumConcurrentJobs = 20
}

# Director configuration
Director {
  Name = bacula-dir
  Password = "DataServerPassword"
}

# Messages configuration
Messages {
  Name = Standard
  director = bacula-dir = all, !skipped, !restored
}
2 vulnerabilities detected
Hardcoded Credentials
Embedding credentials in source code risks unauthorized access
Hardcoded Credentials
Embedding credentials in source code risks unauthorized access
#### 2.3. Start Bacula File Daemon Service
bash
sudo systemctl start bacula-fd
sudo systemctl enable bacula-fd
### 3. Install and Configure Bacula File Daemon on NFS Server
#### 3.1. Install Bacula Client
bash
sudo apt update
sudo apt install bacula-client
#### 3.2. Configure Bacula File Daemon (/etc/bacula/bacula-fd.conf)
Edit the Bacula File Daemon configuration file:
bash
sudo nano /etc/bacula/bacula-fd.conf
Add the following configuration:
bash
FileDaemon {
  Name = NFSServer-fd
  FDport = 9102
  WorkingDirectory = /var/lib/bacula
  PidDirectory = /var/run/bacula
  MaximumConcurrentJobs = 20
}

# Director configuration
Director {
  Name = bacula-dir
  Password = "NFSServerPassword"
}

# Messages configuration
Messages {
  Name = Standard
  director = bacula-dir = all, !skipped, !restored
}
#### 3.3. Start Bacula File Daemon Service
bash
sudo systemctl start bacula-fd
sudo systemctl enable bacula-fd
### 4. Install and Configure Bacula File Daemon on Client Workstation
#### 4.1. Install Bacula Client
bash
sudo apt update
sudo apt install bacula-client
#### 4.2. Configure Bacula File Daemon (/etc/bacula/bacula-fd.conf)
Edit the Bacula File Daemon configuration file:
bash
sudo nano /etc/bacula/bacula-fd.conf
Add the following configuration:
bash
FileDaemon {
  Name = Client-fd
  FDport = 9102
  WorkingDirectory = /var/lib/bacula
  PidDirectory = /var/run/bacula
  MaximumConcurrentJobs = 20
}

# Director configuration
Director {
  Name = bacula-dir
  Password = "ClientPassword"
}

# Messages configuration
Messages {
  Name = Standard
  director = bacula-dir = all, !skipped, !restored
}
2 vulnerabilities detected
Hardcoded Credentials
Embedding credentials in source code risks unauthorized access
Hardcoded Credentials
Embedding credentials in source code risks unauthorized access
#### 4.3. Start Bacula File Daemon Service
bash
sudo systemctl start bacula-fd
sudo systemctl enable bacula-fd
### 5. Verify the Configuration
#### 5.1. Test Connectivity
Ensure that the Bacula Director can communicate with all File Daemons. Use the bconsole command on the backup server to check the status of each client:
bash
sudo bconsole
Once in the Bacula console:
bash
status client=DataServer-fd
status client=NFSServer-fd
status client=Client-fd
#### 5.2. Run a Manual Backup
You can manually start a backup job to verify that everything is working correctly:
bash
run job=BackupDataServer
run job=BackupNFSServer
run job=BackupClient
Follow the prompts to start the backup jobs.
### Summary
- Backup Server: Install and configure Bacula Director, Storage Daemon, and File Daemon.
- Data Server, NFS Server, Client Workstation: Install and configure Bacula File Daemon.
- Configuration: Define jobs, file sets, and clients in Bacula Director configuration.
- Verification: Test connectivity and run manual backups to ensure everything is set up correctly.
This guide provides a comprehensive setup for Bacula on a client-server network, ensuring that critical directories on each server and workstation are backed up efficiently.